## Slide 1: HEMS OPERATIONS
HEMS Authorizations, Authorized WX Sources, & Associated OPSPECS
HEMS WEATHER SUMMIT
Andy Pierce, AFS-250 Policy Branch
December, 2013

## Slide 2: POLICY RELATED TO HEMS WX
A021 HEMS OPERATIONS
A010 AVIATION WEATHER INFORMATION
H113 SPECIAL TERMINAL AREA IFR ROTORCRAFT OPERATIONS IN CLASS G AIRSPACE
EXEMPTIONS
§ 135.213(b) & NWS

## Slide 3: A021 HEMS OPERATIONS
  § e. Minimum weather in Class G = VFR per Table 1- Weather Minimums
 | NON-MOUNTAINOUS |  | MOUNTAINOUS (see 14 CFR 95) | 
Area - | Local | Cross Country | Local | Cross Country
Condition | Ceiling-Visibility |  |  | 
Day | 800 – 2 | 800 – 3 | 800 – 3 | 1000 - 3
Night – Equipped with NVIS or TAWS | 800 – 3 | 1000 – 3 | 1000 – 3 | 1000 – 5
Night- w/o NVIS or TAWS | 1000 – 3 | 1000 – 5 | 1500 – 3 | 1500 – 5

## Slide 4: A021 HEMS OPERATIONS
§f. IFR OPS at locations without weather reporting-
  AUTHORIZED with IAP, and without:
    NWS weather or
    NWS approved weather observation source or
    Weather observation approved by Administrator

## Slide 5: A021 HEMS OPERATIONS
§f. IFR OPS LIMITATIONS
    1) PIC or qualified observer- VFR? per 135.205(b) or,
    2) Use approved weather source if within 15 miles or Area forecast per H113 AND,
    3) IFR- Alternate w/ approved WX observation resource
    4) AFTER LANDING, PIC determines if takeoff minimums per 14 CFR §97 prevail

## Slide 6: A021 HEMS OPERATIONS
§g. IMPACT OF HTAWS / NVIS
  To use Table 1 reduced minimums- OPSPEC A050 (NVG Operations) must be issued

## Slide 7: A021 HEMS OPERATIONS
§h. VFR / Visual transitions </= 3 nm
  1) Day 600 – 2, Night 600 – 3 with-
    PinS approach with “Proceed VFR” transition or
    Standard IAP with VFR transition MAP to site

## Slide 8: A021 HEMS OPERATIONS
§h. VFR / Visual transitions > 3 nm
  2) Table 1 applies
  3) When published on IAP, approved visual segment minimums apply
§i. VFR cruise altitude minimums
  300 day
  500 night

## Slide 9: A010 AVIATION WEATHER INFO
AUTHORIZES VARIOUS WEATHER SOURCES
  NWS
  Internet weather providers
  Specific remote aviation weather observation sites WITH Specific landing sites (conditions and limitations may apply)

## Slide 10: H113 IFR IN CLASS G AIRSPACE
CLASS G OPS AUTHORIZED PROVIDING-
  1) Airport is served by IAP
  2) Airport has approved WX Reporting
  3) Airport provides traffic advisories and status of facilities and services
  4) Facilities and services for SAFE IFR Operations are available
CLASS G OPS at an alternate is authorized if 1) – 4) above are met

## Slide 11: EXEMPTIONS
HAI Consortium Exemption-
  Where weather observation is not available (eg: Hospital)
  Allows qualified PIC or representative to observe weather prior to IFR departure
  Determine that weather is VFR or not

## Slide 12: § 135.213(b) & NWS
Allows application of weather observation taken remote from landing site providing:
  NWS Regional Aviation Meteorologist concurs
NWS POLICY 10-1301 supports this analysis and disposition
NWS may non-concur
NON-CONCUR cannot be over-ridden
NWS CONCURS- Confirmation Letter from NWS to FAA & listed in OpSpec A010

## Slide 13: § 135.213(b) & NWS
ISSUES (PREVIOUSLY RARELY USED PROCESS)
  8900.1 GUIDANCE inadequate
  NWS Regional Meteorologist is a rotational position
  No single access point is available at this time
  MOA or MOU may be advisable

## Slide 14: § 135.213(b) & NWS
PROPOSED GO FORWARD PLAN
  FAA-
    Proposed- 8900.1 guidance revision (in works)
    Proposed- standard Inter-Agency Request Template
    Invite collaborative development of a mutually agreeable linkage
  NWS-
    Review and consider FAA proposals
    Establish a process for consistent evaluation
    Establish a static address or a consistent means of receiving requests for analysis and disposition

## Slide 15: Request for NWS WX valuation
The EVAL REQUEST must:
    Mention 14 CFR 135.213(b) and NWS Policy 10-1301 to orient the Meteorologist
    Provide the location of the landing site (airport or heliport by FAA identifier, if available, and geo-coordinates)
    Provide the location of the nearest aviation weather observation site (again by FAA identifier and geo-coordinates)

## Slide 16: NWS Evaluation
The NWS Regional Aviation Meteorologist will determine whether or not the weather observed at the remote observation site is representative of the weather at the landing site.
After NWS Team concurrence, the result will be forwarded to the FAA FSDO.